## Slide 1
Chapter 6 Functions of Combinational Logic

## Slide 2
Basic rules of binary addition are performed by a half adder, which has two binary inputs (A and B) and two binary outputs (Carry out and Sum).
Half-Adder 半加器
A
B
S
Cout
The logic symbol and equivalent circuit are:
A
B
S
Cout
S
∑= AB’ + A’B = A⊕B
Cout=AB

## Slide 3
n-bit Addition ?
The addition of two n-bit binary numbers generates a n-bit sum and a carry out.
Cout | C3 | C2 | C1 | C0
 | A3 | A2 | A1 | A0
+ | B3 | B2 | B1 | B0
 | S3 | S2 | S1 | S0
1 | 1 | 0 | 1 | 0
 | 1 | 1 | 0 | 1
+ | 1 | 1 | 0 | 1
 | 1 | 0 | 1 | 0
Example: let n = 4

## Slide 4
Full-Adder(全加器)
By contrast, a full adder has three binary inputs (A, B, and Carry in) and two binary outputs (Carry out and Sum).
The truth table summarizes the operation.
1
1
0
0
1
0
0
AB
Cin
10
11
01
00
1
0
1
1
0
1
1
0
1
0
AB
Cin
10
11
01
00
1
0
0
Cout = AB + A’BCin + AB’Cin
= AB + (A⊕B)Cin
∑ = AB’ Cin’ + A’B’Cin + A’BCin’ +ABCin = A⊕B⊕Cin
Notes: Cout没有化到最简是为了后续方便。

## Slide 5
Full-Adder
A full-adder can be constructed from two half adders as shown:
A
B
S
Cout
S
A
B
S
Cout
S
A
B
Sum
Cout
Cin
A
B
S
Cout
S
Cin
Symbol
Cout = AB + (A⊕B)Cin
∑ = A⊕B⊕Cin

## Slide 6
Full-Adder
Example
Solution
For the given inputs, determine the intermediate and final outputs of the full adder.
The first half-adder has inputs of 1 and 0; therefore the Sum =1 and the Carry out = 0.
The second half-adder has inputs of 1 and 1; therefore the Sum = 0 and the Carry out = 1.
The OR gate has inputs of 1 and 0, therefore the final carry out = 1.
A
B
S
Cout
S
A
B
S
Cout
S
1
1
0
1
0
1
0
1
Sum
Cout

## Slide 7
n-bit Combinational Adders（n位加法器）
Perform parallel multi-bit addition
  Parallel Adders (并行加法器，also called Ripple Carry Adder，脉动进位加法器 )
    Simple design
    Time consuming.
  Carry Look ahead Adder (先行进位加法器)
    More complex than Parallel Adders
    Reduces circuit delay

## Slide 8
Parallel Adders 并行加法器
Full adders are combined into parallel adders that can add binary numbers with multiple bits. A 4-bit adder is shown.
A
B
S
Cout
Cin
A
B
S
Cout
Cin
A
B
S
Cout
Cin
A
B
S
Cout
Cin
A1 B1
S1
C0
S2
S3
S4
C1
C2
C3
C4
A2 B2
A3 B3
A4 B4
The carry (C4) is not ready until it propagates through all of the full adders. This is called ripple carry, delaying the addition process.
Notes: 进位信号由低位向高位逐级传递，所以这种加法称为行波进位传递。
串行加法器的延时主要受进位传递延时影响，如果一个1位FA的延时为△，则n位串行加法器的延时为n △ 。

## Slide 9
Carry Look ahead Adder(超前进位加法器)
One method of speeding up the addition process by eliminating this ripple carry delay is called look-ahead carry addition(超前进位加法).
Consider：Ci+1 = AiBi + (Ai  Bi) Ci
Carry generation(进位产生)：
  Let Gi = AiBi= 1，if Gi=1，then Ci+1=1
Carry propagation(进位传递)：
  Let Pi = Ai  Bi ，if Pi=1，then Ci+1=Ci
Notes: n位加法器的逻辑电路的替代设计
以硬件成本增加为代价，使得延时减少。
方式：把FA的进位产生与进位的传递分开
此处的Gi也即书上的Cgi，Pi是书上的Cpi

## Slide 10
Carry Look ahead Adder(先行进位加法器)
HA
HA
PARTIAL FULL ADDER(PFA)
Can this connection eliminate the ripple carry delay ？
Notes: 这个连接方式能不能解决进位传递延时问题？
否。进位方式仍然是行波进位。
解决方案：让Ci只依赖于C0和Ai，Bi

## Slide 11
A 4-bit Carry Look ahead Adder
Ci+1 = Gi + PiCi
Base on this ayalysis:
  C1 = G0+P0 C0
  C2 = G1+P1C1 = G1+P1(G0+P0C0) = G1+P1G0+P1P0C0
  C3 = G2 + P2C2 = G2+P2G1+P2P1G0+P2P1P0C0
  C4 = G3+P3G2+P3P2G1+P3P2P1G0 + P3P2P1P0 C0
Now the ripple problem is solved.
Carry generation(进位产生)
Carry propagation(进位传递)
Notes: 传递延时此时是常数，不依赖于行波进位，只依赖于门电路的延时。

## Slide 12
Ci：2 gate delays.
A 4-bit Carry Look ahead Adder

## Slide 13
Logic diagram for a 4-stage look-ahead carry adder

## Slide 14
A 4-bit Adders(4位加法器)
The logic symbol for a 4-bit parallel adder is shown. This 4-bit adder includes a carry in (labeled (C0) and a Carry out (labeled C4).
The 74LS283 is an example. It features look-ahead carry, which adds logic to minimize the output carry delay. For the 74LS283, the maximum delay to the output carry is 17 ns.
Binary number A
Binary number B
Input carry
4-bit sum
Output carry
1
2
3
4
1
2
3
4
1
2
3
4
C0
C4
S

## Slide 15
An application:
a voting system

## Slide 16
An application: Cascading(级联) four 74LS283 four-bit adders to form 1 16bit adder
Notes: 注意：此时芯片内部为先行进位方式，但是芯片之间仍是行波传递方式。

## Slide 17
An application：Subtractor
Using 2’s complement to realize subtraction
Why c-in always be 1？
Input data
Difference
Notes: 两个二进制数A、B相减，可以转为补码操作A补+(-B)补
进位C-in恒置1，等价于把被减数按位取反+1。

## Slide 18
An application：an adder/subtractor circuit.
A’/S is the mode control. How does it work?
When the A’/S mode control input is a 0 the EX-OR gates do not invert, so the input data are added unchanged. The carry-in bit is forced to logic 0.
Notes: A’/S控制决定了做加法还是减法操作
  A’/S为0时，异或门不进行取反操作，进位为逻辑0，为加法器
  A’/S为1时，异或门进行取反操作，进位为逻辑1，为减法器

## Slide 19
An application：a BCD to Excess-3 code converter

## Slide 20
An application：BCD Adder
BCD Decimal Adder:
  Requires 8 inputs (4 bits per decimal number)
  5 outputs indicate the decimal sum and the carry
  Remember BCD addition rules: Add 0110 to the sum if it is greater than 1010 to correct the carry bit
e.g.：Let A=1000，B=0111。The BCD sum of A+B is (1)0101
 | 1 | 0 | 0 | 0
+ | 0 | 1 | 1 | 1
 | 1 | 1 | 1 | 1
 |  | 1 | 1 | 1 | 1
+ |  | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 0 | 1
Notes: 进位关系不同，故需+6修正

## Slide 21
1、
2、
3、
0111（8421 BCD）=7, 正确。
1101是非法码。需加 6 修正。
产生进位，本位和正确。
0001,错误。需加 6 修正。
产生进位，本位和正确。
错误产生原因：两者进位关系不同

## Slide 22
结论：两个BCD码相加
  当和大于9或进位为1的时候，需要将结果加6进行修正；
  当和小于9则不修正。
修正信号应在有进位信号Cout产生、或两个8421BCD码相加之和为10~15的情况下产生。

## Slide 24
&
&
1
Σ
Σ
Σ
Σ
&
加6修正

## Slide 25
Comparators 比较器
The function of a comparator is to compare the magnitudes of two binary numbers to determine the relationship between them.
A | B | A=B | A>B | A<B
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
Single bit comparator
  A EQ B = A’B’ + AB
  A > B = AB’
  A< B = A’B
How about Two-bit comparator?

## Slide 26
Comparators
A3 B3 A2 B2 A1 B1 A0 B0 | FA＞B FA＜B FA＝B
A3＞B3 × × × A3＜B3 × × × A3＝B3 A2＞B2 × × A3＝B3 A2＜B2 × × A3＝B3 A2＝B2 A1＞B1 × A3＝B3 A2＝B2 A1＜B1 × A3＝B3 A2＝B2 A1＝B1 A0＞B0 A3＝B3 A2＝B2 A1＝B1 A0＜B0 A3＝B3 A2＝B2 A1＝B1 A0＝B0 | 1 0 0 0 1 0 1 0 0 0 1 0 1 0 0 0 1 0 1 0 0 0 1 0 0 0 1
Notes: 对于多位比较，可以先比较最高位，高位相等的条件下，再查看低位比较结果

## Slide 27
F> = F3> + F3=F2> + F3=F2=F1> + F3=F2=F1=F0>
F< = F3< + F3=F2< + F3=F2=F1< + F3=F2=F1=F0<
F= = F3=F2=F1=F0=

## Slide 28
Comparators
IC comparators provide outputs to indicate which of the numbers is larger or if they are equal.
Cascading inputs are provided to expand the comparator to larger numbers.
Outputs
A1
A0
A2
A3
B1
B0
B2
B3
Cascading
inputs
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
The IC shown is the 4-bit 74LS85.

## Slide 29
Comparators
IC comparators can be expanded using the cascading inputs as shown.
The lowest order comparator has a HIGH on the A = B input.
Outputs
A1
A0
A2
A3
B1
B0
B2
B3
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
A5
A4
A6
A7
B5
B4
B6
B7
+5.0 V
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
LSBs
MSBs

## Slide 30
Decoders 译码器
A decoder is a logic circuit that detects the presence of a specific combination of bits at its input.
Two simple decoders that detect the presence of the binary code 0011 are shown. The first has an active HIGH output; the second has an active LOW output.
A1
A0
A2
A3
X
Active HIGH decoder for 0011
A1
A0
A2
A3
X
Active LOW decoder for 0011

## Slide 31
Decoders
Assume the output of the decoder shown is a logic 1. What are the inputs to the decoder?
Question

## Slide 32
Decoders
IC decoders have multiple outputs to decode any combination of inputs.
For example the binary-to-decimal decoder shown here has 16 outputs – one for each combination of binary inputs.

## Slide 33
74LS138
The 74LS138 is a 3-to-8 decoder(1-of-8) with three chip select inputs (two active LOW, one active HIGH).

## Slide 34
Y0’=(C’B’A’)’
Y1’=(C’B’A)’
Y2’=(C’BA’)’
Y3’=(C’BA)’
Y4’=(CB’A’)’
Y5’=(CB’A)’
Y6’=(CBA’)’
Y7’=(CBA)’
=m0’
=m1’
=m2’
=m3’
=m4’
=m5’
=m6’
=m7’
74LS138 and minterms

## Slide 35
A binary decoder can be used to develop some logic expressions.
Eg: Implement the following logic expressions with 74LS138:
  Y1=A’B’+AC+A’C’
  Y2=A’C+AC’
  Y3=B’C+BC’
Application of binary decoder

## Slide 36
Y1 =A’B’+AC+A’C’
=A’B’C+A’B’C’+ABC+AB’C+A’BC’+A’B’C’
=m1+m0+m7+m5+m2+m0
= (m0’m1’m2’m5’m7’)’
Y2 =A’C+AC’
=A’BC+A’B’C+ABC’+AB’C’
= m3+m1+m6+m4
= (m1’m3’m4’m6’)’
Y3 =B’C+BC’
=AB’C+A’B’C+ABC’+A’BC’
=m5+m1+m6+m2
= (m1’m2’m5’m6’)’
Step1:Convert the expressions to standard SOP form

## Slide 37
Y1= (m0’m1’m2’m5’m7’)’
Y2= (m1’m3’m4’m6’)’
Y3= (m1’m2’m5’m6’)’
Step2: Draw the logic circuits with 74LS138 and basic gates
Is there any other solution?

## Slide 38
Y1=A’B’+AC+A’C
=∑(0,1,2,5,7) = m3’m4’m6’
Y2=A’C+AC’
= ∑(1,3,4,6) = m0’m2’m5’m7’
Y3=B’C+BC’
=∑(1,2,5,6) = m0’m3’m4’m7’
Y1= (m0’m1’m2’m5’m7’)’
Y2= (m1’m3’m4’m6’)’
Y3= (m1’m2’m5’m6’)’

## Slide 39: Exercise
  Implement the following logic expressions with 74LS138
    X = f(a,b,c) = ∑(0,3,5,6,7)

## Slide 40
Decoders
A specific integrated circuit decoder is the 74HC154 (shown as a 4-to-16 decoder).
It includes two active LOW chip select lines which must be at the active level to enable the outputs. These lines can be used to expand the decoder to larger inputs.
CS2
A1
A0
A2
A3
CS1
X/Y
EN
74HC154

## Slide 41
Implementing Boolean functions using decoders
use 74HC154 to implement F(A, B, C, D) = m(1,2,5,7)
F

## Slide 42
1 1 1
Chip2
0 0 0
1
1 1 1
Chip1
0 0 0
0
D8～D15
D0～D7
x y z
W
0 1 1 1
0 0 0 0
1 1 1 1
1 0 0 0
Select signal
=>Enable
Select chip 1:
Select chip 2:
Cascading two 74LS138 to implement one 4-to-16 decoder

## Slide 44
Decoders
BCD-to-decimal decoders accept a binary coded decimal input and activate one of ten possible decimal digit indications.
A1
A0
A2
A3
Example
Solution
Assume the inputs to the 74HC42 decoder are the sequence 0101, 0110, 0011, and 0010. Describe the output.
All lines are HIGH except for one active output, which is LOW. The active outputs are 5, 6, 3, and 2 in that order.

## Slide 45
BCD Decoder/Driver
Another useful decoder is the 74LS47. This is a BCD-to-seven segment display with active LOW outputs.
BCD inputs
Outputs to seven segment device
GND
VCC
BCD/7-seg
BI/RBO
BI/RBO
LT
RBI
LT
RBI
74LS47
灯测试
异步灭零输入
灭零输入/异步灭零输出

## Slide 46
BCD Decoder/Driver
Blanked
Blanked
The 74LS47 features leading zero suppression, which blanks unnecessary leading zeros but keeps significant zeros as illustrated here. The BI/RBO output is connected to the RBI input of the next decoder.

## Slide 47
BCD Decoder/Driver
Blanked
Blanked
Decimal point
Trailing zero suppression blanks unnecessary trailing zeros to the right of the decimal point as illustrated here. The RBI input is connected to the BI/RBO output of the following decoder.

## Slide 48
Encoders编码器
An encoder accepts an active logic level on one of its inputs and converts it to a coded output, such as BCD or binary.

## Slide 49
Encoders
The decimal to BCD is an encoder with an input for each of the ten decimal digits and four outputs that represent the BCD code for the active digit.
The basic logic diagram is shown. There is no zero input because the outputs are all LOW when the input is zero.
A1
A0
A2
A3
1
2
3
4
5
6
7
8
9

## Slide 50
Encoders
A1
A0
A2
A3
Example
Solution
Show how the decimal-to-BCD encoder converts the decimal number 3 into a BCD 0011.
The top two OR gates have ones as indicated with the red lines. Thus the output is 0111.
1
2
3
4
5
6
7
8
9
0
0
0
0
0
0
0
0
1
0
0
1
1

## Slide 51
8-3 binary encoders
A0 = D1 + D3 + D5 + D7
A1 = D2 + D3 + D6 + D7
A2 = D4 + D5 + D6 + D7

## Slide 53
Encoders
The 74HC147（十进制-BCD编码器） is an example of an IC encoder. It is has ten active-LOW inputs and converts the active input to an active-LOW BCD output.
It is a priority encoder(优先编码器). This means that if more than one input is active, the one with the highest order decimal digit will be active.
Decimal input
BCD output
GND
VCC
HPRI/BCD
74HC147

## Slide 54
priority encoder 优先编码器
highest priority
non-priority encoder
priority encoder

## Slide 55
74LS148 8-3 priority encoder

## Slide 56
priority
encoder
Fire
Theft
Gas leakage
TV
AC
proc
119
110
call user
other
other
Application : priority encoder

## Slide 57
Code converters代码转换器
There are various code converters that change one code to another. Two examples are the four bit binary-to-Gray converter and the Gray-to-binary converter.
Example
Show the conversion of binary 0111 to Gray and back.
Solution
0
0
0
1
1
1
Binary-to-Gray Gray-to-Binary
MSB
LSB
MSB
LSB
1
0
0
0
1
0
0
1
1
1

## Slide 58
A multiplexer (MUX) selects one data line from two or more input lines and routes data from the selected line to the output.
The particular data line that is selected is determined by the select inputs.
Multiplexers数字多路器

## Slide 59
For a 2n-to-1 multiplexer, there are 2n data input lines and n selection lines whose bit combination determines which input is selected.
  4-to-1 Multiplexer needs 2 selection lines.
  8-to-1 Multiplexer needs 3 selection lines.
Multiplexers

## Slide 60
2-1 demultiplexer
Truth table
Input（2lines）
0
1
Select
D0
D1

## Slide 61
A
D
A
D
Y
1
0
'
+
=
Input
Select
2-1 demultiplexer

## Slide 62
D0
D2
D1
D3
0
1
0
1
A1
A0
D2
A1
A0
Y
0
0
0
0
D0
1
1
1
1
D1
D3
Select signal
4-1 demultiplexer
+ + +

## Slide 63
Multiplexers
Two select lines are shown here to choose any of the four data inputs.
Data select
Data inputs
Data output
D1
D0
D2
D3
S1
S0
Question
Which data line is selected if S1S0 = 10?
D2
1
0

## Slide 64
Example: Quad 2-to-1 MUX
Uses four 2-to-1 MUXs with common select (S) and enable (E).
Select line chooses between Ai’s and Bi’s. The selected four-wire digital signal is sent to the Yi’s
Enable line turns MUX on and off (E=1 is on).
Notes: 使用4个2-1选择器，共享使能和选择信号。
S选择线决定把Ai还是Bi送往Yi
使能信号E打开或关闭多路器。

## Slide 65
8-1 Multiplexer 74LS151

## Slide 66
Implementing Boolean functions with Multiplexers
Using an 8-to-1 multiplexer to realize the Boolean function F=f(x,y,z)=∑(1,2,4,5,7)
= 0
令

## Slide 67: Exercise
Using an 8-to-1 multiplexer to realize the Boolean function
F=f(x,y,z)=∑(0,3,5,6,7)

## Slide 68
AB
00
01
11
10
CD
00
01
11
10
AB
C
00
01
11
10
0
1
4-input
3-input
2-input
D
C+D
0
1
0
1
A
B
CD
C+D
How can implement a 3-input function with a 4-1 multiplexer?

## Slide 69
D
C+D
0
1
0
1
A
B
CD
C+D
0
1
A
1-input

## Slide 70
E.g. Using an 4-1 multiplexer to realize the Boolean function F=f(x,y,z)=∑(1,2,4,5,7)
1
1
1
1
XY
Z
00
01
11
10
0
1
1
z'
X
Y
0
1
0
1
z
1
z
D0=z
D1=z’
D2=1
D3=z
F=X’Y’D0+X’YD1+XY’D2+XYD3
=X’Y’Z+X’YZ’+XY’+XYZ
X
Y
z
z’
1
z
D3
D2
D1
D0
4-1
MUX
A1
A0
EN
F

## Slide 71
Exercise: Using an 4-1 multiplexer to realize the Boolean function
F = f(x,y,z) = ∑(1,2,6,7)

## Slide 72
A demultiplexer (DEMUX) performs the opposite function from a MUX. It switches data from one input line to two or more data lines depending on the select inputs.
The 74LS138 was introduced previously as a decoder but can also serve as a DEMUX.
When connected as a DEMUX, data is applied to one of the enable inputs, and routed to the selected output line depending on the select variables.
Note that the outputs are active-LOW .
Demultiplexers（多路分配器）
74LS138
Data select lines
Enable
inputs
Data outputs
Notes: 定义：把数字数据以特定的时序从一个输入传送到不同输出中的一条输出线上的一种数字电路。

## Slide 73
Determine the outputs, given the inputs shown.
Demultiplexers
Example
74LS138
Data select lines
Enable inputs
Data outputs
A
0
Y
0
Y
1
Y
2
Y
3
Y
4
Y
5
Y
6
Y
7
A
1
A
2
G
1
G
2A
G
2B
LOW
LOW
Solution

## Slide 74
Parity Generators/Checkers奇偶发生器/校验器
Parity is an error detection method that uses an extra bit appended to a group of bits to force them to be either odd or even. In even parity(偶校验), the total number of ones is even; in odd parity(奇校验) the total number of ones is odd.
11010011
S with odd parity =
S with even parity =
01010011
Example
The ASCII letter S is 1010011. Show the parity bit for the letter S with odd and even parity.
Solution

## Slide 75
Parity Generators/Checkers
Checker: The 74LS280 can test codes with up to 9 bits. The even output will normally be HIGH if the data lines have even parity; otherwise it will be LOW. Likewise, the odd output will normally be HIGH if the data lines have odd parity; otherwise it will be LOW.
Generator: To generate even parity, the parity bit is taken from the odd parity output. To generate odd parity, the output is taken from the even parity output.
74LS280
Data inputs
S Even
S Odd

## Slide 76
Selected Key Terms
Full-adder
Cascading
Ripple carry
Look-ahead carry
A digital circuit that adds two bits and an input carry bit to produce a sum and an output carry.
Connecting two or more similar devices in a manner that expands the capability of one device.
A method of binary addition in which the output carry from each adder becomes the input carry of the next higher order adder.
A method of binary addition whereby carries from the preceding adder stages are anticipated, thus eliminating carry propagation delays.

## Slide 77
Selected Key Terms
Decoder
Encoder
Priority encoder
Multiplexer (MUX)
Demultiplexer (DEMUX)
A digital circuit that converts coded information into a familiar or noncoded form.
A digital circuit that converts information into a coded form.
An encoder in which only the highest value input digit is encoded and any other active input is ignored.
A circuit that switches digital data from several input lines onto a single output line in a specified time sequence.
A circuit that switches digital data from one input line onto a several output lines in a specified time sequence.

## Slide 78
1. For the full-adder shown, assume the input bits are as shown with A = 0, B = 0, Cin = 1. The Sum and Cout will be
a. Sum = 0 Cout = 0
b. Sum = 0 Cout = 1
c. Sum = 1 Cout = 0
d. Sum = 1 Cout = 1
Quiz
A
B
S
Cout
S
A
B
S
Cout
S
0
1
0
Sum
Cout

## Slide 79
2. The output will be LOW if
a. A < B
b. A > B
c. both a and b are
correct
d. A = B
Quiz
A1
B1
A2
B2
A3
B3
A4
B4
Output

## Slide 80
3. If you expand two 4-bit comparators to accept two 8-bit numbers, the output of the least significant comparator is
a. equal to the final output
b. connected to the cascading inputs of the most
significant comparator
c. connected to the output of the most significant
comparator
d. not used
Quiz

## Slide 81
4. Assume you want to decode the binary number 0011 with an active-LOW decoder. The missing gate should be
a. an AND gate
b. an OR gate
c. a NAND gate
d. a NOR gate
Quiz
A1
A0
A2
A3
X
?

## Slide 82
5. Assume you want to decode the binary number 0011 with an active-HIGH decoder. The missing gate should be
a. an AND gate
b. an OR gate
c. a NAND gate
d. a NOR gate
Quiz
A1
A0
A2
A3
X
?

## Slide 83
6. The 74138 is a 3-to-8 decoder. Together, two of these ICs can be used to form one 4-to-16 decoder. To do this, connect
a. one decoder to the LSBs of the input; the other decoder to the MSBs of the input
b. all chip select lines to ground
c. all chip select lines to their active levels
d. one chip select line on each decoder to the input MSB
Quiz

## Slide 84
7. The decimal-to-binary encoder shown does not have a zero input. This is because
a. when zero is the input,
all lines should be LOW
b. zero is not important
c. zero will produce
illegal logic levels
d. another encoder is used
for zero
Quiz
A1
A0
A2
A3
1
2
3
4
5
6
7
8
9

## Slide 85
8. If the data select lines of the MUX are S1S0 = 11, the output will be
a. LOW
b. HIGH
c. equal to D0
d. equal to D3
Quiz
Data
select
Data
inputs
Data
output
D1
D0
D2
D3
S1
S0

## Slide 86
9. The 74138 decoder can also be used as
a. an encoder
b. a DEMUX
c. a MUX
d. none of the above
Quiz

## Slide 87
10. The 74LS280 can generate even or odd parity. It can also be used as
a. an adder
b. a parity tester
c. a MUX
d. an encoder
Quiz

## Slide 88
Answers:
1. c
2. c
3. b
4. c
5. a
6. d
7. a
8. d
9. b
10. b
Quiz

## Slide 89: Homework
self-test
8
14
16
20
24
32